## Slide 1: Spacecraft Design Lab – Communication Protocols
D.J. Morvay

## Slide 2: Option #1 – Space Packet Protocol
General Information
  Primary Packet Header – 6 octets (bytes)
  Packet Data Field - 1 to 65536 octets
  Consists of at least 7 and at most 65542 octets

## Slide 3: Space Packet Primary Header

## Slide 4: Space Packet Primary Header – Part #1
Packet Version Number (3 bits) - Set to ‘000’
Packet Identification Field (13 bits)
  Packet Type (1 bit)
    ‘0’ -> Telemetry,
    ‘1’ -> Telecommand
  Secondary Heading Flag (1 bit)
    ‘0’ -> No Secondary header
    ‘1’ -> Secondary header present
  Application Process Identifier (11 bits, Mission Specific)
    Identify sending and receiving application process

## Slide 5: Space Packet Primary Header – Part #2
Packet Sequence Control Field (16 bits)
  Sequence Flags (2 bits)
    ’00’ -> Continuation Segment
    ‘01’ -> First segment
    ‘10’ -> Last segment
    ‘11’ -> Unsegmented
  Packet Sequence Count (14 bits)
    If Packet Type == ‘0’ (telemetry), then field contains packet sequence count
    If Packet Type == ‘1’ (telecommand), then field contains packet sequence count OR packet name
Packet Data Length (16 bits, Mission Specific)
  Length count C that equals one fewer than the length (in octets) of the Packet Data Field

## Slide 6: Packet Data Field
Packet Secondary Header (Variable Length, Mission Specific)
  Consists of…
    Time Code Field
    Ancillary Data Field
    Time Code + Ancillary Data
  Consistent mission specific data in Ancillary Field
User Data Field (Variable Length)
  Application data supplied by the sending user (AKA all other data)

## Slide 7: Key Takeaways of SPP
Can send long messages (images and memory data)
  Separate the messages into a group of Space Packets
  Ex: ½ image in message #1 and ½ image in message #2
Constructed to support telemetry and telecommands
Mission specific PIDs
  Ex: PID 0x10 == Battery Information
  Ex: PID 0x11 == Power Off Commands
Consistent data with Secondary Headers